Group 3
Key Activation System Explained
Step 1
For the key activation system, we establish the discrete signal and sampling frequency of the audio file.
Step 2
We use Fourier fast transform (FFT) to transform the signal into the frequency domain and then viewed the spectrum of the signal.

Step 3
Based on the given frequency of the signal which is 392Hz, we use filter designer to establish First Stopband Frequency (fstop1), First Passband Frequency(fpass1), Second Passband Frequency (fpass2), Second Stopband Frequency (fstop2), Sampling Frequency (Fs) for the filter which are:
Fs = 14,000Hz
Fstop1 = 352Hz
Fpass1 = 372Hz
Fpass2 = 412Hz
Fstop2 = 432Hz

Step 4
Generate Matlab code from the filter designer function including the system objects (Hd). Use the Load command to load Hd into Matlab.

Step 5
Use the filter function in Matlab with the system object Hd as numerator coefficients, denominator coefficients as 1 and the signal (S) as parameters.

Step 6
Transform the filtered signal into the frequency domain with the FFT function and plot the filtered signal.