Group 3
Trigger System: Block Diagram Explained
The trigger system for our device receives a discrete signal (digital signal) intended to wake up the device and check for the activation key. from the discrete signal.
Step 1
From the discrete signal, we establish both the silence level (digital Silence Threshold) of the environment and the sampling frequency (Fs). Also, we establish the number of samples in the signal (N) and its duration (N/Fs).
Step 2
Production of the signal equivalent to Fs/4. This is to conserve energy for the device.
Step 3
We compute the power of the sampled audio signal. If the power of the signal is greater than the silence threshold, the device is triggered to wake up and wait for the activation key. Otherwise, the device does nothing and remains asleep.
 Power =

Matlab Code Explained
The main objective is to compute the power of air audio signal.
 Step1: we are taking the sample of arrays.
       S =[s1,s2,s3,…,sn] and we can also find the help option in MATLAB for the function description.
        e.g.: help audioread
 Step2: To compute the power of an audio signal.
We create a new script in MATLAB with the filename myTrigger. Also, the function in the script should be written as myTrigger() (i.e the same name as the filename). The audio file should be in same folder as the script file (myTrigger).
       -----function myTrigger()
       digitalSilenceThreshold = 0;
# Normally, the digital silence threshold ratio in MATLAB is zero whereas if we are in a room or in some other areas the digital silence threshold will vary according to the environment.
        [S,Fs]= audioread(‘audioFile.wav’);
 # Fs is the sample frequency and it is said to be defined as number of samples per second. The audioread() function is used to get the array values of signal S.
        N=length(S);
# The length function is used to calculate number of samples in signal (S).
        duration=N/Fs ;
# we are using the above formula to find duration by dividing the length by sample frequency. The duration is in seconds.

Step3: To find the power of an audio signal.
 # Initially the power is set to 0. We need to calculate the total power . The total power is calculated by using below formula.

        Power =
    Finally, if the power is greater than digital silence threshold, it will execute/trigger the device.