## Slide 1: IntelliSense
Optimal Environmental Quality
GROUP 3
Fahadh Mohamed
Kuiyu Ding
Shola Olayemi
Bello Nuhu
Sudharshan A V

## Slide 2: Project Objective
To detect environmental indices by collecting relevant parameters such as;
Environmental sound quality
Temperature and Humidity
Set different thresholds to determine how good the environmental indices are represented.

## Slide 3: Project Implementation
Based on the project design, the electronics of the project were assembled and integrated around the microcontroller.
These included the following;
Hardware:
Tiva Microcontroller - ARM® Cortex®-M4F Based MCU TM4C123G Launchpad
Temperature and Humidity Sensor
Ultrasonic Sensor
Main board, display board and amplifier board
Software:
Energia IDE was used to program the microcontroller and in C language. It was also used to display the environmental parameters obtained by the sensors.

## Slide 4: Sensors Integrated
•Temperature and Humidity Sensor - DHT11
•Ultrasonic Sensor – Electret microphone amplifier(MAX4466)

## Slide 5: ADC and Voltage Values via Putty
Microcontroller has a 12 bits ADC = 212 = 4096
VCC * ADC/4096

## Slide 6: Display on PC via Bluetooth Connection

## Slide 7: OLED DISPLAY
We uploaded image in a website to convert into hexadecimal code and we displayed our logo in lcd display through energia.

## Slide 8: Temperature and humidity :
We connected temperature and humidity sensor to the extended board. The data shows the output of temperature and humidity sensor.
-4°C – -1°C: Bad
0°C – 6°C: Fair
7°C – 15°C: Ideal
16°C – 22°C: Fair
23°C – 30°C: Bad

## Slide 9: System Operation
The device is triggered based on the power of an audio signal compared to the silence threshold.
It starts to listen for the key by passing the signal through a filter. If the key is detected by the filter, then the device begins measuring process.
It measures the sound quality in decibels
It measures and outputs the temperature and humidity of the environment.

## Slide 10: Data Treatment
ADC
TRIGGER
Recording & Analyzing the Signal
Estimates of different measures
S(t)
Fs sampling frequency imposed on microcontroller
S(ms)
S(mte)
Key detected
Key not detected recompute power for another sample
Filter

## Slide 11: Trigger System
Power
Computation
Is power greater than the silence threshold
S(mts)
Discrete Signal
Silence-Threshold
Recompute the power for another sample
Key detection process
Sample Signal (Fs/4)
Establish Silence Level
Wake Device

## Slide 12
1.Design idea
Filter design and implement
Key or nosie
Only 440HZ key "la" can pass

## Slide 13: 2.Matlab simulation
By using filterDesigner, filters can be easily designed in Matlab.
In this case , we need to choose these parameter when designing the filter:
Samplign frequency => 2B
Design method : FIR;
Response type: Bandpass
Other parameters..
Filter Designeer tool
Compare the response of the input signal and the output signal in the frequency domain.
Result means input signal could pass the filter.

## Slide 14: 3. Principle of FIR filter and implementation
Convolution in time-domain = mutiplying in frequency-domain
N: length of sample—NBSAMPLE 1000;
M: order of filter ---- number of coefficient;
Inplement the left formula on energia by c language

## Slide 15: 4.Calculate power
Envaluate if the key be detected by calculate the output power of the filter signal. Key is detected when power is more than power1

## Slide 16: Energy Conservation
The product consumes 456mw of power
The product is expected to run for 13 hours a day.
Consequently, the power consumption is 6000mwh.
Therefore, energy consumed in 1 year = 6000 x 365 = 2,190,000mwh
i.e. 2.19Kwh
This equivalent to 0.0009 Metric Tons of CO2 = 1 pound of coal burned = 0.001 acres of US forest in 1 year.
To conserve the battery, we recommend a solar solution to charge the battery.

## Slide 17: Power Consumption & Battery Autonomy
Battery Lithium-ION
EEMB 3.7V 2000mAh
103454
Battery Lithium-ION
Rechargeable with connector
Storage & Application
No leaks, excellent economic performance and long service life.
PCM protection function:
over charge, over discharge, over current, short circuit protection,
over temperature protection.
Keep cells in 40-60% state of charge during long-term storage.
Recommend charging the battery every 3 months
after receiving the battery and keeping the voltage 3.7-4.0V.
Notes: No leaks, excellent economic performance and long service life. PCM protection function: over charge, over discharge, over current, short circuit protection, over temperature protection.
Keep cells in 40-60% state of charge during long-term storage. We recommend charging the battery every 3 months after receiving the battery and keeping the voltage 3.7-4.0V. Store the battery in a cool, dry place. // SUITABLE for Bluetooth speaker, dash cam, Wi-Fi enabled smart home systems, PDAs and digital cameras, GPS, tracking devices, pulse monitors.

## Slide 18: Transmission and Display of Data
The details of the quality of the sound, humidity and temperature are analyzed based on ideal conditions to advise users to go running or not.
The values and decisions would be transmitted to a cell phone via Bluetooth.

## Slide 19: Future Planning
Collaborate or sell the product to a fitness app development company
Adaptation of the product to various environments.